The technical features of SGP-83 (two-boiler single-turbine unit)

| Parameter | Measuring unit | value |
| --- | --- | --- |
| The nominal electrical power, including electrical power: | MW | 83,7 |
| The power of GTU (total power) | MW | 60,8 |
| The power of STU | MW | 22,9 |
| The electrical efficiency of GTU | % | 34,5 |
| The exhaust gas flow rate | Kg/s | 204 |
| The boiler exhaust gas temperature | °С | 120 |
| The fuel flow rate (natural gas) | Kg/s | 3,6 |
| The steam-generating capacity of STU | Kg/s | 25,1 |
| The electrical efficiency of STU | % | 47,0 |
| The nominal fuel gas flow rate for 1 GTU | Kg/s | 1,795 |
| The designed inlet fuel gas pressure of STU | Kg/sm²(isobar) | 31 |
| The ambient temperature | °С | +15 |
| SLL; Service Life Limit | h | For GT and ST = 200000 |
| Time between overhaul | h | For GT = 48000 |
| The weight of the main equipment | tons | 1150 |