Technical characteristics

| Parameters | Type of compressor |
| --- | --- |
|  | 47-71-1С | 47С СПЧ 2,5/116 |
| Volume capacity referred to 20°C and 0.1013 MPa, mil m³/day | 3,44 | 2,51 |
| Volume capacity referred to the initial conditions, m³/min. | 45 | 44 |
| Final gas pressure at the compressor outlet, MPa abs. | 9,5 | 8,25 |
| Pressure ratio | 1,98 | 2,34 |
| Polytropic efficiency, no less than | 0,8 | 0,805 |
| Power consumed by the compressor, kW | 3650 | 3300 |
| Gas pressure at the compressor inlet, MPa | 4,8 | 3,53 |
| Gas temperature at the compressor inlet, °C | 15 | 6 |
| Gas density referred to 20°C. 0.1013 MPa, kg/m³ | 0,682 | 0,682 |
| Nominal rotor speed, min -¹ | 10290 | 10350 |