The Main Technical Characteristics of the GPU-32 «Ladoga»

| Name of parameter | GPU-32 | GPU-32-02 | GPU-32-03 |
| --- | --- | --- | --- |
| Nominal coupling power in the station conditions, MW, no less than | 31,2 |
| Volume capacity referred to the nominal conditions (0.1013 МMPa, 20 °С), mil m³/day. | 78.9 | 62,0 | 66,0 |
| Polytropic efficiency of the centrifugal compressor, no less than, % | 85 | 80 | 80 |
| GTU effective efficiency when operating at nominal power in the station conditions, %, | 36,0 |
| Nominal gas working pressure, abs., at the centrifugal compressor outlet, MPa | 11,86 | 7,45 | 7,45 |
| Pressure ratio | 1,4 | 1,44 | 1,38 |
| Nominal speed of the GTU power turbine rotor | 5714 |
| Temperature downstream the turbine, °С (nom./max) | 510/600 |
| Fuel gas flow, kg/s | 1,78 |