Technical characteristics of Axial Compressors

| Parameters | Compressor Type |
| --- | --- |
|  | К-3750-1 | К-4300-1 | К-4950-1 |
| Compressed Fluid | Air |
| Volumetric Suction Capacity, m³/min. | 3750 | 4280 | 4930 |
| Final Air Pressure, MPa abs. | 0,46 | 0,48 | 0,54 |
| Initial Parameters: temperature, °С | 30 | 30 | 30 |
| pressure, MPa abs. | 0,098 | 0,098 | 0,098 |
| Gas density at 20°С and 0.1013 MPa, kg/m³ | 1,2046 | 1,2046 | 1,2046 |
| Rated Rotor Speed, rpm. | 5400 | 5100 | 5200 |
| Compressor Consumed Power, MW | 15,8 | 18,7 | 23,6 |
| Drive Type: steam turbine | P-16-3,4/0,8-1 | P-18-3,4/0,8-1 П-23- 8,8/0,8-1 | P-23-8,8/0,8-1 |
| Rated power, MW | 15,8 | 18,7 | 23,6 |
| Operating rotor speed, rpm. | 3900-5400 | 4600-5200 | 4600-5200 |
| Overall Dimensions, m: , м: |
| Foundation Length | 9 | 12,53 | 12,9 |
| Foundation Width | 5,24 | 4,6 | 4,6 |
| Floor Level of the Mechanical Equipment Room | 7,2 | 7,2 | 7,2 |
| Crane Hook Lifting Height in reference to the mechanical equipment room floor level | 5,5 | 5,5 | 5,5 |
| Weight, tonnes |
| Of the as-delivered compressor | 51 | 50 | 50 |
| Of the compressor itself | 30,0 | 28,0 | 28,0 |
| Of the heaviest assembly unit during assembling and operation | 30/11,2 | 35/11,5 | 35/13 |