Main technical characteristics of the units

| Parameters | К890- 122-1 | К411- 122-1 | К410- 121-1 | К410- 121-2 | 415- 61-1 | К354- 101-1 | К380- 103-1 | К320- 131-1 | 340- 81-5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mass capacity, kg/f | 19,4 (18,25) | 8,93 | 8,93 | 10,1 | 11,72 | 9,53 (9,73) | 9,73 | 10,086 | 13,5 |
| Volume capacity at suction conditions, m³/min: . | 760 (820) | 372 | 372 | 395 | 372 | 355 (345) | 345 | 320 | 300 |
| Final gas pressure, MPa, abs.** | 3,63 | 3,53 | 3,7 | 3,7 | 1,57 | 3,82 | 3,82 | 3,1 | 1,3 |
| Gas density, kg/m³ | 0,98 (0,957) | 0,91* | 0,91* | 1,12** | 0,91* | 0,83 (0,913) | 0,98 | 0,75 | 1,42 |
| Initial gas parameters |
| Temperature, °C | 15 | 15 | 15 | 30 | 15 | 15 | 15 | 15 | 35 |
| Pressure, MPa, abs. | 0,157 | 0,157 | 0,157 | 0,147 | 0,206 | 0,186 | 0,186 | 0,25 | 0,1275 |
| Nominal rotor speed (L.P. cylinder/ H.P. cylinder), min-¹ | 5240 HPC 9270 HPC | 11129 | 10345 | 9677 | 10345 | 8559 HPC 18419 HPC | 8100/ 17445 | 10800 | 4800/ 9370 |
| Power consumed by the rotor, MW | 10,0 (11,2) | 4,95 | 5,17 | 4,95 | 4,243 | 5,2 (5,3) | 5,3 | 5,3 | 3,0 |
| Overall dimensions, m: |
| Foundation length | 16,3 | 11 | 11 | 11 | 8,2 | 12,2 | 12,2 | 12,2 | 7,0 |
| Foundation width | 4,5 | 2,9 | 2,9 | 2,9 | 2,9 | 4,0 | 4,0 | 4,0 | 2,8 |
| Height | 2,6 | 2,0 | 2,0 | 2,0 | 4,0 | 4,8 | 4,8 | 4,8 | 2,0 |
| Hoisting height of the crane hook over the floor level of the machine room | 5,0 | 4,9 | 4,9 | 4,9 | 4,2 | 3,5 | 3,5 | 3,5 | 4,2 |
| Design mass, t: |
| Compressor in the scope of supply (without el. motor drive) | 77,3 | 38,89 | 37,65 | 37,65 | 26,23 | 34,8 | 35,0 | 35,0 | 29,0 |
| The heaviest part for: |
| Mounting | 36 (L.P.C. unit) | 24 (compressor unit) | 22,4 (compressor unit) | 22,4 (compressor unit) | 14,5 compressor unit) | 10,2 (el.motor stator) | 10,2 (el.motor stator) | 25 (compressor unit) | 7,15 (main el.motor) |
| Operation | 10 (upper part of the L.P.C. casing) | 4,3 (el.motor rotor) | 4,3 (el.motor rotor) | 4,3 (el.motor rotor) | 3,17 (el.motor rotor) | 3,5 (upper part of the L.P.C. casing in assy) | 3,5 (upper part of the L.P.C. casing in assy) | 5,2 (HPC package) | 2,5 (upper part of the L.P.C. casing in assy) |

* Operation on gas with density of 0.824; 1.02; 1.12 kg/m³ is also available alongside with the above-mentioned values .

** НаOperation on gas with density of 1.22; 1.35 kg/m³ is also available alongside with the above-mentioned values.