The technical features of GTEPS-32

| Parameter | Measuring unit | value |
| --- | --- | --- |
| The nominal electrical power, in stationary conditions (+ 15°С according to ISO) (gross weight) | MW | 30,5 |
| The electrical efficiency of GTU, in stationary conditions | % | 34,5 |
| The exhaust gas flow rate | Kg/s | 102 |
| The fuel flow rate (natural gas) | Kg/s | 1,795 |
| The designed inlet fuel gas pressure of GTU | Kg/sm²(изб) | 31 |
| Lube-oil system of turbo units |  | forced |
| The oil for application |  | ТП-22С |
| SLL; Service Life Limit | h | For GT and ST = 200000 |
| Time between overhaul | h | For GT = 48000 |
| The weight of the main equipment (without the generator and reducer) | Tons | 132 |