The technical features of SGP-42 (single-turbine unit)

| Parameter | Measuring unit | value |
| --- | --- | --- |
| The nominal electrical power, including electrical power: | MW | 41,9 |
| The power of GTU (total power) | MW | 30,4 |
| The power of STU | MW | 11,5 |
| The electrical efficiency of GTU | % | 34,5 |
| The exhaust gas flow rate | Kg/s | 102 |
| The boiler exhaust gas temperature | °С | 120 |
| The fuel flow rate (natural gas) | Kg/s | 1,795 |
| The steam-generating capacity of STU | Kg/s | 12,6 |
| The electrical efficiency of STU | % | 46,7 |
| The nominal fuel gas flow rate for 1 GTU | Kg/s | 31 |
| Lube-oil system of turbo units |  | forced |
| The oil for application |  | ТП-22С |
| SLL; Service Life Limit | H | For GT and ST = 200000 |
| Time between overhaul | h | For GT = 48000 |
| The weight of the main equipment | Tons | 700 |