THE MAIN PARAMETERS OF THE  MS5002E GAS TURBINE UNIT

| Наименование параметра | Значение |
| --- | --- |
| Nominal drive coupling power referred to GOST R 52200–2004, MW, no less than | 32,0 |
| GTU effective efficiency referred to GOST R 52200–2004 when operating at nominal power, %, no less than | 36,0 |
| Nominal speed of the LPT rotor, rpm | 5714 |
| Variation range of the LPT rotor speed, % of the nominal value | от 70 до 105 |
| Sense of LPT rotor rotation, if viewed from the side of the loading device | Clockwise, GOST 22378-77 |
| Time of startup and acceleration to the minimum operating mode (from the hot standby condition), min | 5 |
| Nominal fuel gas flow, kg/s | 1,74 |
| Fuel gas pressure, MPa | от 3,1 до 3,5 |
| Irrecoverable oil losses, kg/h, no more than | 0,25 |
| Nominal/maximum temperature of combustion products downstream the turbine (across section of the turbine exhaust duct), °С | 510/600 |
| Combustion air flow in the nominal operating mode, kg/f | 100 |
| Combustion products flow (across section of the turbine exhaust duct), kg/s | 101,7 |
| Air pressure ratio in the axial compressor | 17,0 |
| Harmful substance content of exhaust gas (measured in the dry sample at 0°С, 0.1013 MPa and standard oxygen concentration of 15%): –NOх, mg/m³, no more than; – СО, mg/m³, no more than; | 50 34,7 |
| Rate of harmful substance emission with combustion products at nominal power conditions: –NOх, g/s, no more than; –СО, g/s, no more than; | 3,7 2,6 |