Тechnical characteristics

| Name of parameter | 400-21-1С | 400СПЧ 1,44/76-32С (СПЧ – replaceable flow passage) | 400СПЧ 1,38/76-32С |
| --- | --- | --- | --- |
| Capacity referred to the normal conditions (0.1013 MPa and 20 °С), million m³/day | 78.9 | 62,0 | 66,0 |
| Volume capacity referred to the initial conditions, m³/min | 505 | 748 | 780 |
| Power consumed, MW | 30,4 | 29,5 | 28,3 |
| Polytropic efficiency, no less than,% | 85,0 | 85,0 | 84,0 |
| Pressure ratio | 1,4 | 1,44 | 1,38 |
| Final gas pressure (abs.), MPa | 11,86 | 7,45 | 7,45 |
| Compressor inlet temperature, °С | 5 | 15 | 20 |
| Compressor rotor speed, rpm. | 5550 | 5550 | 5550 |

Note

The compressor parameters values can be changed for specific operating conditions required.

The main parameters of the 400-21-1С compressor correspond to the specified values at the following initial design conditions

| Name of parameter | Value |
| --- | --- |
| Gas pressure, abs., at the inlet of the compressor suction branch pipe, MPa | 8,45 |
| Gas temperature at the inlet of the compressor suction branch pipe, °С | 5 |
| Gas density referred to 20 °С and 0.1013MPa, kgг/m³ | 0,689 |
| Design speed of the compressor rotor, rpm | 5550 |
| Note: Design speed of the compressor rotor is 97-98 % of the turbine nominal speed in accordance with para 5.23 of “Standard Technical Requirements for Gas Turbine GPU and their Systems” STO Gazprom 2.3.5-138–2007. |