The Main Technical Characteristics of the 	Compressors

| Name of parameter | Value |
| --- | --- |
|  | 170-31-1С | 125-31-1С | 151-21-1С | 151СПЧ1,6 5/4,83С | 385-21-1 |
| Volume capacity referred to 20°C and 0.1013 MPa, mil m³/day | 5,25 | 4,3 | 7,87 | 4,43 | 32 |
| Volume capacity referred to the initial conditions, m³/min. | 150 | 123 | 151 | 96,1 | 385 |
| Final gas pressure at the compressor outlet, MPa, abs. | 3,74 | 3,74 | 4,62 | 4,83 | 7,45 |
| Pressure ratio | 1,7 | 1,7 | 1,4 | 1,65 | 1,44 |
| Polytropic efficiency, no less than | 0,82 | 0,84 | 0,84 | 0,82 | 0,85 |
| Power consumed by the compressor, MW | 3900 | 3400 | 3750 | 3250 | 15,2 |
| Gas pressure at the compressor inlet, MPa | 2,2 | 2,2 | 3,3 | 2,93 | 5,174 |
| Gas temperature at the compressor inlet, °C | 2 | 2 | 10 | 8,5 | 15 |
| Gas density referred to 20°C and 0.1013 MPa, kg/m³ | 0,681 | 0,681 | 0,6913 | 0,6913 | 0,682 |
| Nominal rotor speed, min -¹ | 10300 | 10400 | 10200 | 10300 | 5050 |
| Overall dimensions of the compressor unit, mm.: Length Width Height | 2230 1590 1435 | 2230 1590 1435 | 2037 1590 1435 | 2037 1590 1435 | 2900 2530 3150 |
| Mass of the heaviest parts, kg Unit casing package |  |  | 26800 12200 9900 |
| Hoisting height of the crane hook from the floor level of the machine room for package disassembly, mm | 2200 | 2200 | 1500 | 1500 |  |
| Mass of the heaviest parts, kg for mounting (inside the container) For operation (outside the container) | 9550 1000 | 9740 1000 | 8500 1000 | 8500 1000 | 24600 8800 |