Steam Turbines Driving the Axial Compressors

| Model | Rated Power, MW | Maximum Power (in cond.mode), MW | Steam Rate at Nominal Operation Parameters, t/h | Steam Rate at Maximum Operation Parameters, t/h | Temperature, °С | Shaft Speed, min-¹ | Initial Value, and Adjustable Range Of Steam Rate (t/h) and Initial Value, and Adjustable Range Of Steam Rate (t/h) and of Inlet Nozzle Pressure (MPa) | Steam Consumption by the Central Heating System, t/h (parameters °С/MPa) | Cooling Water Rate, t/h | Specific Weight of the Turbine, t/MW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Р-23- 8,8/0,8 |  | 23,6/15,8 | 94,7/123,4 | 8,83 | 535 | 4600- 5200 | 0,59-1,08 | 86,4 | 4900 | 1,78 |
| Р-18- 3,4/0,8 |  | 18,7/12,7 | 85,5/140,9 | 3,43 | 435 | 4600- 5200 | 0,59-1,08 | 114,5 | 4900 | 1,93 |
| Р-16- 3,4/0,8 |  | 15,8/10,8 | 73,8/118,4 | 3,43 | 435 | 3500- 5400 | 0,59-1,08 | 94,7 | 3800 | 2,23 |
| Р-10- 3,4/0,8 |  | 11,0/7,8 | 50,8/86,9 | 3,43 | 435 | 3500- 5300 | 0,118- 0,245 | 66,5 | 3300 | 3,04 |