Technical characteristics of the electric motor

| Name of parameter | UOM | Value |
| --- | --- | --- |
| Supply voltage at all operating conditions | V | 3300 |
| El. motor power rating | kW | 4000 |
| Maximum continuous power | kW | 4200 |
| Nominal efficiency | p.u. | 0,958 |
| Nominal torque | Nm | 4658 |
| Nominal current | А | 970 |
| Maximum continuous current | А | 1020 |
| Rotor moment of inertia | kg·m² | 48 |
| Mass | kg·m2 | 15500 |
| Protection degree as per GOST 14254 | - | IP22 |
| Cooling system | - | air |
| Maximum allowable axial displacement of the rotor | mm | ±2,5 |
| El. motor mounting version | - | IM1001 |

Electric motor protection

| Type of protection | Protection implementation | Location |
| --- | --- | --- |
| Current protection against external multi-phase shorting | Current cutoff without time delay | Frequency converter |
| Current protection against single-phase ground short circuit | Current protection without time delay, operating for trip | Frequency converter |
| Protection against overload | Current overload 123 % — warning is generated, current overload 126 % — emergency trip | Frequency converter |
| Current protection against phase failure | Operates for trip without time delay | Frequency converter |
| Protection against excessive rotor vibration | Two – level protection: - warning; - operates for trip without time delay | Magnetic bearings CS |
| Protection against magnetic bearings overheating |  | Magnetic bearings CS |
| Protection against excessive temperature or cooling system failure |  | ACS |